## Slide 1
PART 3 . SIM vs MEASURED
Comparing simulation and bench, empty phantom
Do the two agree? The signal interpolates equally well on both; the apparent gap is data coverage, not simulation fidelity
6.7 vs 6.0 mm
k-NN signal floor: sim ~ measured
distinct positions
the real driver of the CNN gap
R2 = 0.65
a learnable sim->measured transfer

## Slide 2
The two setups, side by side
The physical A3 phantom on its grid, and the HFSS model of the same phantom
Measured: A3 phantom + 6x6 grid + antennas
Simulated: HFSS phantom, oil, antennas, tumor

## Slide 3
Two sampling grids, and their overlay
Same phantom, different coverage; the right panel registers both into one physical frame

## Slide 4
What differs between the two
Same antenna design, but grid, depth coverage, band and noise differ
 | Simulated (HFSS) | Measured (bench VNA)
Antennas | Sam's Medium Antennas (HFSS model) | Sam's Medium Antennas (physical build)
Grid | uniform 10 mm lattice, 91 positions | 6x6 cells, 4 corners each; 51 measured
Depth | 13 planes, z = -15 to +45 mm | single height, ~5 to 20 mm (near the patch)
Frequency | 2 to 8 GHz, 3001 points | 0.1 to 8 GHz, 791 points
Noise / drift | none (deterministic solve) | measurement noise + cross-session drift
Repeats | one solve per position | 16 takes x 3 sessions per position
The 4 antennas are the SAME design in both; a fair sim vs measured comparison controls for the grid, depth, band and noise.

## Slide 5
Reflection per antenna, sim vs measured
Same design, yet the measured ports differ from each other; the sim ones are near-identical

## Slide 6
Transmission (coupling) per pair, sim vs measured
Four representative antenna-to-antenna terms; couplings also differ between domains

## Slide 7
Detectable difference by reflection S-parameter
Each reflection Sii localizes on its antenna, in measured (top) and simulated (bottom)

## Slide 8
Detectable difference by transmission S-parameter
Each coupling Sij peaks between its two antennas (sim remapped to physical numbering)

## Slide 9
The numbers, signal vs. model
Does the SIGNAL interpolate, and can the CNN learn it? (empty phantom)
Probe | Sim empty | Measured empty
k-NN (training-free signal floor) | 6.7 mm | 6.0 mm
CNN LOSO (new session, seen positions) | - | 3.9 mm
CNN LOPO single-position (unseen position) | - | 9.9 mm
CNN 8-fold (full depth stack, ~1000 pos) | 3.9 mm | -
What is k-NN?
A training-free baseline: to locate a held-out spot it just averages the (x,y) of the most similar measured signals. Nothing is fit, so it measures how well the SIGNAL alone pins down location, a floor any trained model should beat.
What the numbers mean
Signal floor is the same: sim 6.7 vs measured 6.0 mm; the two agree closely.
LOSO (3.9) sees a new session at KNOWN spots (easy); LOPO single-position (9.9) reaches an UNSEEN spot (hard, ~50 distinct positions).
Sim hits 3.9 on unseen spots only via ~1000 distinct positions.
The sim vs measured CNN gap is distinct-position COVERAGE, not fidelity. To match 3.9 mm on the bench: denser grid / more depths, not a better model.

## Slide 10
Test 1: zero-shot, train on sim only, test on the bench
If the CNN sees only simulated tumors, can it locate a real one? Direct transfer collapses
What this tests
Train a CNN on simulated tumor dS only; no measured data is seen in training.
Then hand it the measured S-parameters and ask for (x,y).
The result
In-domain (held-out sim) it localizes to 15 mm, so the pipeline works.
On the bench it hits 74 mm, worse than the 34 mm predict-centre chance line.
Predictions collapse to one biased corner: the measured signal is out-of-distribution for a sim-only model.
The antenna domain gap breaks direct transfer. The sim signal must be calibrated toward the bench first (next slides).

## Slide 11
How the sim to measured map is learned
A linear transfer fit on the empty baseline and tested on frequencies it never saw
1
Pair the empty baselines
Sim empty phantom and measured empty phantom are the same physical state (no tumor), so their S-parameters can be matched frequency by frequency.
2
One vector per frequency
At each of 512 frequencies (2 to 8 GHz), stack the real and imaginary parts of the 16 S-parameters into a 32-D vector. Sim = input x, measured = target y.
3
Split the frequencies 70 / 30
Fit on 70% of the frequencies; hold out the other 30% for testing. The map never sees the test frequencies while it is being fit.
4
Fit the linear map
Ridge (L2) regression learns a 32x32 matrix W and offset b that best convert the sim vector into the measured vector.
5
Test on the held-out 30%
Apply W and b to the unseen frequencies and compare to the true measured values, giving R2 = 0.65.
The equation
y = W x + b
x = sim [Re, Im of 16 S-params] (32-D); y = predicted measured; W (32x32) and b learned on the train frequencies.
Why R2 = 0.65 is meaningful
R2 is computed only on frequencies the map never used while fitting, so it measures genuine generalization, not curve-fitting.
A model that merely memorized the training frequencies would score near 0 on the held-out set. The flexible MLP did exactly that (R2 < 0).
So R2 = 0.65 says a fixed linear transform already recovers most of the measured signal from the sim, on data it has not seen.

## Slide 12
Can a model bridge the gap? (exploratory)
The learned map applied to one port, and its accuracy on unseen frequencies
How to read it
Left: the dashed line is the simulated S11 after the map (W x_sim + b). A perfect map would land on the measured (red) curve; it moves toward it but does not fully match.
Right: predicted vs measured on the held-out frequencies. Points on the diagonal are exact; the R2 = 0.65 spread shows the map captures most, not all, of the relationship.
A flexible MLP overfits and fails to generalize (R2 < 0).
Preliminary: only the empty baseline is cleanly paired. Nonlinear domain adaptation needs far more paired data (multiple sessions, matched tumor positions).

## Slide 13
Beet (dielectric) vs metal tumor, sim and measured
How much differential signal a realistic dielectric target produces relative to metal

## Slide 14
Part 3, bottom line
1
Sim and measured agree at the signal level: the empty phantom interpolates to ~6 mm on both (k-NN), indicating the simulated signal is realistic.
2
The detectable-difference pattern matches: bench and sim place the tumor's strongest change in the same regions (toward the antenna sides).
3
The CNN gap is data coverage, not fidelity: sim's 3.9 mm comes from ~1000 distinct positions; measured's 9.9 mm from only ~50. Same model, different coverage.
4
Sim predicts beet approximately equals metal, but the bench does not: in sim the beet produces 93% of the metal signal; on the bench only 42%, flagging an object-size / depth mismatch or an optimistic sim beet model.
5
A sim to measured transfer is learnable: a linear map already reaches R2 = 0.65 on unseen frequencies, a promising if preliminary calibration path.
github.com/pmart1534/microwave-phantom-localization-cnn-mlp