## Slide 1
TUMOR LOCALIZATION IN BREAST PHANTOMS
CNN vs MLP
A matched, head-to-head comparison of two machine-learning approaches
for microwave tumor localization
Peter Martin · University of Utah · Electrical & Computer Engineering
Preprocessing pipeline v1 (includes session-mean subtraction)

## Slide 2
THE PROBLEM
Find a hidden tumor inside a breast phantom
Goal: locate a small tumor surrogate (metal fishing weight) placed inside a realistic breast phantom, without opening it up.
Microwave imaging: low-cost, non-ionizing alternative screening modality.
The tumor perturbs how microwaves reflect and transmit through the tissue, but the change is tiny and buried in drift and noise.
Worst case: a glandular insert (dense tissue) further masks the tumor signal.
Task: given one measurement, which of ~33–51 grid positions holds the tumor?
A3 breast phantom with F5 glandular insert and measurement grid

## Slide 3
THE SOLUTION
Let a machine learn the fingerprint of every position
Classic inverse-scattering reconstruction is slow and fragile. Instead, we treat localization as a pattern-recognition problem: measure the phantom with the tumor at every known position, then train a model to recognise each position's electromagnetic fingerprint.
16
S-parameters per sweep
791
frequency points, 0.1–8 GHz
~2–3%
chance-level accuracy

## Slide 4
PART 1
Methods
The measurement, the two models, and how they differ

## Slide 5
METHODS
The physical measurement
Empty A3 phantom: adipose bowl, 6×6 in grid, 4 antennas at the rim
4-port Hunter VNA sweeps 0.1–8 GHz (791 points) through 4 antennas around the phantom.
Each sweep captures all 16 S-parameters: 4 reflections (S11…S44) plus transmissions between every antenna pair.
Tumor surrogate is moved through a grid of cell corner positions; 16 repeat trials per position.
Baseline (empty-phantom) sweeps recorded each session for calibration.
Each setup measured in 3–4 independent sessions on different setups/times; this matters later (LOSO).

## Slide 6
METHODS
Two ways to turn a measurement into a position
Both models receive the SAME preprocessed measurement and output a probability for every grid position. They differ in how they look at the data.
CNN
Convolutional Neural Network · MATLAB
Sees the measurement as a 2-D image: y axis = channels, x axis = frequency
Convolution filters slide along frequency, learning local patterns
MLP
Multi-Layer Perceptron · Python
Sees the measurement as one long flattened vector of numbers
Every input connects to every neuron: the network has no built-in idea that neighboring frequencies are related, so any such structure must be learned from scratch

## Slide 7
METHODS
The CNN
Input is an image: one row per data channel (e.g. |S11|, ∠S11, …), one column per frequency point (791).
Two convolution layers (32 filters each) detect local patterns such as resonance shifts and ripples anywhere along the spectrum, sharing weights across frequency.
Batch-normalisation + ReLU after every layer; 30% dropout fights overfitting.
One network, trained 100 epochs with Adam (batch 16) on the GPU; softmax outputs one probability per grid position.

## Slide 8
METHODS
The MLP
Input is a flat vector: all channels and frequencies concatenated (thousands of features). No spatial structure is assumed.
Two dense layers (256 → 128, ReLU): every feature can interact with every other, but nothing is shared or localized.
Early stopping on a held-out validation split prevents overtraining.
Ensemble: 3 networks with different random seeds are averaged, plus a logistic-regression model; the ensemble vote is the prediction.

## Slide 9
METHODS
CNN vs MLP: structural differences
 | CNN | MLP
How it sees data | 2-D image (channels × frequency) | 1-D flattened vector
Inductive bias | Local patterns, shared across frequency | None; fully general
Parameters | Small conv filters + FC (~0.5–2 M) | Huge first layer (features × 256)
Training | Fixed 100 epochs, single network | Early stopping, 3-seed ensemble + LogReg
Framework | MATLAB Deep Learning Toolbox (GPU) | Python scikit-learn (CPU)
Same job, opposite philosophies: the CNN assumes frequency-local structure; the MLP assumes nothing. Everything else in this study is held identical.

## Slide 10
PART 2
The data pipeline
What happens to a measurement before any 'AI' ever sees it. Identical for both models.

## Slide 11
DATA PIPELINE
Four steps from raw sweep to model input
Steps 1–2 remove everything that is not the tumor; step 4 (per-session z-score) is the key drift defense: each session is standardized by its own statistics. Applied identically to CNN and MLP.
Upgrading the CNN to this pipeline was worth +17 pts on F5 single-antenna (59→76%) with fold-to-fold σ cut from 40% to 9%, and +15 pts on F4 single-antenna (82→97%). Its catastrophic cross-session failures disappeared entirely.

## Slide 12
DATA PIPELINE
Three input representations
RAW
Magnitude + phase of each calibrated S-parameter.
The measurement as the VNA reports it. Used for the main results.
PHYSICS
Adds real & imaginary parts and the IFFT time-domain (TDR) envelope.
Derived at no cost from the same data; covered at the end.
TDR-ONLY
Just the time-domain envelope, a pulse-echo view.
An ablation: how much lives in time domain alone?
Same numbers, two shapes:
CNN: channels stacked as image rows × 791 frequency columns
MLP: the same rows laid end-to-end as one long vector
Antenna subsets work the same way: '2 antennas' keeps only S-parameters among ports 1 & 3; '1 antenna' keeps only S11.

## Slide 13
DATA PIPELINE
How we score: Leave-One-Session-Out
A random 75/25 split mixes trials from the same session into train AND test, so the model can cheat off session drift, inflating accuracy.
LOSO trains on N−1 sessions and tests on the session it has never seen; every session takes a turn. We report per-position majority vote over its 16 trials.
We have thoroughly stress-tested LOSO and verified that it works: under LOSO, models cannot exploit session drift, and drift-only information scores near chance.

## Slide 14
DATA PIPELINE
Three phantom setups, increasing difficulty
A3 Empty
adipose only
51 positions · 3 sessions
A3 + F4
small glandular insert
39 positions · 4 sessions
A3 + F5
large glandular insert
33 positions · 3 sessions (latest)

## Slide 15
PART 3
Results
Per-position vote accuracy (%) under LOSO · identical raw inputs (mag + phase) · chance = 2–3%

## Slide 16
RESULTS · RAW INPUTS
All 4 antennas: full S-parameters (16)
Phantom setup | Positions | CNN (%) | MLP (%) | CNN − MLP
A3 Empty | 51-way | 99.3 ± 1.1 | 99.3 ± 0.9 | +0.0
A3 + F4 | 39-way | 97.4 ± 3.0 | 97.4 ± 1.8 | +0.0
A3 + F5 | 33-way | 100.0 ± 0.0 | 96.0 ± 2.9 | +4.0
Mean ± std over LOSO folds. Bold = better method.
With the full antenna array, both methods are near-perfect on every phantom; drift and glandular masking are fully compensated. CNN edges ahead on the hardest setup (F5).

## Slide 17
RESULTS · SPATIAL VIEW
Error Locations: all 4 antennas
Dot color = how strongly the tumor physically changes the signal (detectable difference). Dot size = CNN LOSO accuracy at that position. Dashed outline = glandular insert.
Detectable change still dips inside the glandular insert (blue), but with 16 complementary views the classifier compensates: accuracy dots stay large almost everywhere. MLP versions look qualitatively identical.

## Slide 18
RESULTS · RAW INPUTS
All 4 antennas: reflection only (S11, S22, S33, S44)
Phantom setup | Positions | CNN (%) | MLP (%) | CNN − MLP
A3 Empty | 51-way | 100.0 ± 0.0 | 99.3 ± 0.9 | +0.7
A3 + F4 | 39-way | 98.7 ± 1.5 | 93.6 ± 4.3 | +5.1
A3 + F5 | 33-way | 100.0 ± 0.0 | 88.9 ± 2.9 | +11.1
No through-phantom transmission paths; each antenna only listens to its own echo.
Dropping transmission barely touches the CNN (F5 stays at 100%), while the MLP gives up 4-7 points on the glandular phantoms. Four reflection coefficients are enough for a CNN.

## Slide 19
RESULTS · SPATIAL VIEW
Error Locations: all 4 antennas, reflection only
Reflection-only detectable change (max of S11, S22, S33, S44). The insert still carves a low-signal pocket, but CNN accuracy dots stay large.

## Slide 20
RESULTS · RAW INPUTS
2 antennas (ports 1 & 3): full S-parameters
Phantom setup | Positions | CNN (%) | MLP (%) | CNN − MLP
A3 Empty | 51-way | 99.3 ± 1.1 | 99.3 ± 0.9 | +0.0
A3 + F4 | 39-way | 95.5 ± 1.3 | 93.6 ± 4.3 | +1.9
A3 + F5 | 33-way | 96.0 ± 7.0 | 81.8 ± 4.3 | +14.2
Antennas 1 & 3 sit on opposite sides of the phantom (most informative pair).
Halving the antennas separates the methods: the CNN stays high (96%+ everywhere) while the MLP drops 14 points on F5. Convolutional structure extracts more from less hardware.

## Slide 21
RESULTS · SPATIAL VIEW
Error Locations: 2 antennas (1 & 3)
With two antennas a low-signal pocket appears inside the glandular insert, and accuracy dots shrink with it.

## Slide 22
RESULTS · RAW INPUTS
2 antennas (1 & 3): reflection only (S11, S33)
Phantom setup | Positions | CNN (%) | MLP (%) | CNN − MLP
A3 Empty | 51-way | 99.3 ± 1.1 | 99.3 ± 0.9 | +0.0
A3 + F4 | 39-way | 92.3 ± 5.9 | 93.6 ± 5.9 | −1.3
A3 + F5 | 33-way | 90.9 ± 5.3 | 74.8 ± 6.2 | +16.1
The toughest 2-antenna condition: two reflection coefficients and nothing else.
The CNN holds 91-99% while the MLP falls to 75% on F5. F4 is the single config in the study where the MLP edges the CNN (93.6 vs 92.3).

## Slide 23
RESULTS · SPATIAL VIEW
Error Locations: 2 antennas (1 & 3), reflection only
With only S11 and S33, the low-signal pocket deepens and CNN errors start to appear inside the insert.

## Slide 24
RESULTS · RAW INPUTS
1 antenna: S11 only
Phantom setup | Positions | CNN (%) | MLP (%) | CNN − MLP
A3 Empty | 51-way | 98.0 ± 2.0 | 99.3 ± 0.9 | −1.3
A3 + F4 | 39-way | 96.8 ± 4.9 | 91.0 ± 5.6 | +5.8
A3 + F5 | 33-way | 75.8 ± 9.1 | 58.6 ± 9.4 | +17.2
A single reflection coefficient: the minimal possible hardware.
The extreme case: one antenna, one S-parameter. The CNN holds 76–98%; the MLP falls to 59% on F5. The gap grows exactly as the task gets harder, and the F5 errors cluster inside the glandular insert (next slide).

## Slide 25
RESULTS · SPATIAL VIEW
Error Locations: 1 antenna (S11)
Single antenna (S11): small blue dots cluster inside the insert. Where physics buries the tumor, the classifier fails.

## Slide 26
PART 4
Physics-informed features
Squeezing more out of the same measurement: no new hardware, no new data collection

## Slide 27
PHYSICS-INFORMED FEATURES
One complex measurement, five physical views
Each calibrated S-parameter Y(f) is one complex spectrum. From it we derive, at zero measurement cost: magnitude & phase (resonance behaviour), real & imaginary parts (full complex information), and the inverse-FFT envelope, a time-domain reflectometry (TDR) view where the tumor appears as an echo at its round-trip delay.
Real example: A3+F5 phantom, S11, tumor at grid position R3C4 (calibrated response Y)
The 'physics' input feeds all five views to both models: the CNN as extra image rows, the MLP as extra vector features. Identical information, matched again.

## Slide 28
PHYSICS-INFORMED RESULTS
Same tests, physics inputs
All-4-antenna physics: both models at ceiling, 97–100% (F5 reaches 100 / 100). Below: the configs where it matters. Reflection-only: next slide.
2 antennas (1 & 3), physics input
Phantom setup | Positions | CNN (%) | MLP (%) | CNN − MLP
A3 Empty | 51-way | 99.3 ± 1.1 | 99.3 ± 0.9 | +0.0
A3 + F4 | 39-way | 98.1 ± 1.3 | 92.3 ± 3.1 | +5.8
A3 + F5 | 33-way | 98.0 ± 3.5 | 85.9 ± 7.6 | +12.1
1 antenna (S11), physics input
Phantom setup | Positions | CNN (%) | MLP (%) | CNN − MLP
A3 Empty | 51-way | 98.7 ± 1.1 | 98.7 ± 1.8 | +0.0
A3 + F4 | 39-way | 95.5 ± 4.4 | 91.7 ± 5.8 | +3.8
A3 + F5 | 33-way | 79.8 ± 3.5 | 62.6 ± 8.0 | +17.2

## Slide 29
PHYSICS-INFORMED RESULTS
Reflection only + physics features
All 4 antennas, reflection only (S11, S22, S33, S44), physics input
Phantom setup | Positions | CNN (%) | MLP (%) | CNN − MLP
A3 Empty | 51-way | 100.0 ± 0.0 | 99.3 ± 0.9 | +0.7
A3 + F4 | 39-way | 98.1 ± 1.3 | 94.2 ± 3.3 | +3.9
A3 + F5 | 33-way | 100.0 ± 0.0 | 87.9 ± 6.6 | +12.1
2 antennas (1 & 3), reflection only (S11, S33), physics input
Phantom setup | Positions | CNN (%) | MLP (%) | CNN − MLP
A3 Empty | 51-way | 100.0 ± 0.0 | 98.7 ± 1.9 | +1.3
A3 + F4 | 39-way | 94.2 ± 3.2 | 90.4 ± 3.3 | +3.8
A3 + F5 | 33-way | 97.0 ± 5.3 | 79.8 ± 7.6 | +17.2
With physics features, reflection-only costs the CNN almost nothing (F5: 100% with four antennas, 97% with two); the MLP pays 8-12 points. A reflection-only system is practical with a CNN.

## Slide 30
PHYSICS-INFORMED RESULTS
What the derived features buy, and what TDR alone can't
Physics vs raw (percentage points gained)
F5, 2 antennas: CNN +2.0 (96→98) · MLP +4.1 (82→86)
F5, 1 antenna: CNN +4.0 (76→80) · MLP +4.0 (59→63)
F5, all 4: MLP +4.0 (96→100), joining CNN at 100%
Easy setups (empty, F4 full-array): no change, already at ceiling.
Physics features help most exactly where raw inputs struggle.
TDR-only ablation (selected)
F4, 1 antenna: CNN 84 / MLP 64 (vs 97 / 91 raw): a big loss for both.
But the CNN mines far more from TDR alone (F5 all-4: 98 vs MLP's 76).
Additional finding: hierarchical (quadrant → position) classification
Two-stage 'find the corner first' scheme tested on both models.
It never helps, and hurts the hardest cases: CNN −6 on F5, MLP −6 on F4-single.
Wrong quadrant = unrecoverable. Single-stage wins under LOSO.

## Slide 31
CONCLUSIONS
What we learned
CNN ≥ MLP, everywhere
On matched inputs the CNN ties easy cases and wins hard ones by up to 17 points.
The gap grows with difficulty
Fewer antennas + bigger glandular insert = bigger CNN advantage.
Preprocessing drives robustness
Per-session z-score eliminated the CNN's catastrophic cross-session failures.
Physics features add accuracy at no cost
Derived views (+TDR) add up to 4 points on the hardest configurations.
Errors follow the physics
Misses cluster inside the glandular insert, where detectable signal change collapses.
Fewer antennas is viable with a CNN
2 antennas: 96–98% on every phantom. Even 1 antenna: 76–98%.